## Slide 1: Cone-beam computed tomography in the diagnosis of diseases of the maxillofacial region.

## Slide 15: Basic interface when working on a tomograph Galileos, Sirona

## Slide 21: The interface of the panoramic tomogram option (the names may differ slightly in different devices) consists of several windows.

## Slide 23: three-dimensional rendering - dental assistant

## Slide 26: Interface for planning of TMJ treatment (Gendex CB-500 device)

## Slide 27: CONDYLOGRAPHY is a recording of TMJ movements.

## Slide 28: CONDYLOGRAPHY is a recording of TMJ movements

## Slide 43: CLCT: coronary, sagittal and axial sections. Centering for occlusive tooth caries 4.5

## Slide 44: Periapical abscess of tooth 4.5 with a fistula in the soft tissues of the body of the LF vestibularly (reliably visualized on the sagittal section - white arrow) and in the mandibular canal.

## Slide 45: Two fistulas in soft tissues Additional canal in the middle third of the distal root of the tooth 3.6 (black arrow), lateral granuloma (white arrow)

## Slide 46: Chronic periodontitis of tooth 3.3: a - fragment of OPTG; b - KLKT, sagittal section: the additional root is visualized orally, its channel is not sealed.

## Slide 47: C-shaped configuration of the tooth root 4.6: a - 2 root canals are visualized on the tangent section, which merge into the apical third; b - on the axial section - 1 channel C-shaped

## Slide 48: External and internal resorption of the tooth root 4.5:

## Slide 49: Fracture of the root of the tooth 1.7: a - longitudinal section: dilated periodontal fissure of the apical third of the root (distally and at the apex); b - sagittal section: longitudinal iatrogenic fracture of the palatine root, which caused the inflammatory process

## Slide 50: The usual structure of the lower molars involves the presence of two roots and three root canals. Quite often in the distal root of these teeth there are two channels (38% of the first lower molars and 28% of the second lower molars), which are not detected in two-dimensional images.

## Slide 51: Removal of filling material for the apex of the distal root of the tooth 3.7: on the coronary section - in the mandibular canal, on the sagittal - reliably does not penetrate into the lumen of the channel.

## Slide 53: Denticle at the mouth of the distal root canal of tooth 4.7 (intersection of coordinate axes

## Slide 54: Application in periodontology. Performing 2D radiography can lead to incorrect assessment of the degree of destruction of bone tissue due to errors due to the projection overlap and, as a result, to inaccuracies in determining reliable anatomical landmarks. Only 3D-visualization allows you to make sections perpendicular to the axis of the dental arch and accurately measure bone defects on the vestibular and oral sides (dehiscence, fenestration) (drawings).

## Slide 55: Resorption of the walls of the alveoli of the tooth 3.5 orally and distally by 2/3 of the root length, vestibular and mesial - by 1/2

## Slide 56: Chronic periodontitis of tooth 4.6 (furcation lesions). Chronic periodontitis of both roots.

## Slide 57: Apical granuloma of tooth 2.2 with a fistula in the soft tissues of the RF vestibular

## Slide 58: Preparation of dental implant surgery and evaluation of its effectiveness. Identification of optimal access and study of anatomical features of RF for sinus lifting operations.

## Slide 59: Preparation of dental implant surgery and evaluation of its effectiveness. Identification of optimal access and study of anatomical features of RF for sinus lifting operations.

## Slide 60: Tracing "of the mandibular canals, virtual implant planning

## Slide 61: . Root cyst of the frontal part of the woofer (including the roots of the teeth 3.2-4.1, with thin and exploding cortical plates vestibularly and lingually), the threat of pathological fracture

## Slide 62: Search for retained and dystopian teeth and planning the operation of their removal overcomplete incisors-microdentia, dystopia (rotation of 180 °), eruption into cavities

## Slide 63: Acute arthritis of the left TMJ - local osteoporosis and usurpation of the cortical plate.

## Slide 64: Bilateral recurrent dislocation

## Slide 65: apical granuloma (red arrow), squeezing the lower wall of the HPV; distal-buccal canal - uneven filling to the apical third.

## Slide 67: Chronic hyperplastic maxillary sinusitis, hyperplasia of the lower nasal concha, conha bullosa of the middle nasal concha

## Slide 68: Volumetric computed tomography (CT) of the paranasal sinuses, an objective radiological method that allows you to get a reliable picture of the condition of the paranasal sinuses and structures of the nasal cavity.

## Slide 71: CLCT in otorhinolaryngology