## Slide 1: Topic 4. Methods of controlling the level of glucose in the blood

## Slide 2: Blood glucose monitoring.
Continuous online monitoring of glucose ( CGMS) is a method of monitoring efficiency treatment sugar diabetes with the help of of a special sensor, which is introduced under skin and measures level glucose every 5 minutes (288 times per day) for 6 days . Then information is transferred to the computer , formed graphic report which mathematically processed and reviewed a doctor Based on received data doctor-endocrinologist gives corresponding recommendations and, if necessary , corrects treatment _

## Slide 3: Glucometer and rules for work with it.
Device for automatic detection sugar is easy to use . Just in case you do not know how to use a glucometer correctly, there are instructions for the device and details video lessons . When it occurs additional questions related to the conduct procedures , according to clarifications better consult a doctor . On the contrary case you risk get unreliable data which directly affect the tactics of combating diabetics manifestations .

## Slide 4: Modern methods of controlling the level of glucose in the blood
Before blood sampling necessary wash and dry hands and process puncture site with 70% alcohol. Before piercing is necessary massage the area where it will be performed pick up blood _ Puncture is performed with the help of special lancet, blood is applied to the test strip inserted into the device . Test strips of the glucometer are inserted into a special hole front side up . The bar should enter completely (up to the stop), as with incomplete establishment and lack of contact can be obtained false results . It can be a signal that it is entered correctly serve click or display glow . A drop is applied to the strip of blood that is absorbed through the intake hole automatically. You should n't to press a strip to the finger or oil drop of blood , as it will distort the result. Modern glucometers served sound signal when insufficient or excessive quantity blood _ Some devices allow add blood, if in the first case fences her it turned out not enough After causing of blood on the test strip and drawing its in the device , everything else actions device will conduct independently and will show the result on the display . are used two units measurements - weight (mg / dl ) and molar (mmol / l). When setting up device set units measurement , time and date of measurement , which stored in memory device .
In order to to understand how to choose a glucometer, you need to know the features of each device - size memory , dimensions , as well which expendable materials for it used - test strips , lancets .

## Slide 5
Thank you for attention