## Slide 1: Lecture №3. Packaging, labeling of finished medicinal products. Closing means. Packaging materials in pharmacy.
MINISTRY OF HEALTH OF UKRAINE
ODESSA NATIONAL MEDICAL UNIVERSITY
Department of Pharmacy Organization and Economics
Prepared by senior teacher Oksana Stepanova

## Slide 2
Pharmaceutical packaging (or drug packaging) is the packages and the packaging processes for pharmaceutical preparations. It involves all of the operations from production through drug distribution channels to the end consumer.
Finished Product is means a Licensed Product in a finished pharmaceutical dosage form that is suitable for commercial sale following Regulatory Approval thereof. It is the medicinal product that has undergone all stages of production, including packaging in its final container. The specifications for release of the finished product must comply with the regulations. The specifications of the finished product at manufacture may be different from those of the medicinal product at expiry.
Bulk product is any product that has completed all the processing stages up to, but not including, final packaging.

## Slide 3
Primary packaging is the packaging in direct contact with the product itself and is sometimes referred to as consumer or retail packaging. The main purpose of primary packaging is to protect and/or preserve, contain and inform the consumer. Typical containers are ampoules, vials, bottles,
Secondary packaging component means a packaging component that is not and will not be in direct contact with the dosage form (boxes…..).
Tertiary packaging facilitates the protection, handling and transportation of a series of sales units or secondary packaging in order to group everything into unit loads during transit. This type of packaging is rarely seen by the consumer.
Types of packaging

## Slide 8
Functions of packaging
1.
Containment
Protection
Presentation and information
Compliance
Protection of patients
Detection of counterfeiting

## Slide 10
Containment
The containment of the product is the most fundamental function of packaging for medicinal products. The design of high-quality packaging must take into account both the needs of the product and of the manufacturing and distribution system. This requires the packaging:
not to leak, nor allow diffusion and permeation of the product;
to be strong enough to hold the contents when subjected to normal handling;
not to be altered by the ingredients of the formulation in its final dosage form.
Protection
The packaging must protect the product against all adverse external influences that may affect its quality or potency, such as:
light
Moisture
oxygen
biological contamination
mechanical damage.
The compatibility of the packaging with the active pharmaceutical ingredients is very important in maintaining the integrity of the product.

## Slide 11
Storage. Packaging materials should be stored in accordance with GMP for storage areas. The characteristics of the active pharmaceutical ingredients will determine whether different packaging will be needed. For example, the packaging requirements of medicinal products kept at temperatures between 2 and 8°C may differ from those of products intended for tropical countries or light-sensitive products

## Slide 12
The container and its closure must not interact physically or chemically with the substance within in any way that would alter its quality. The following terms include general requirements for the permeability of containers:
A container for pharmaceutical use is an article which holds or is intended to contain and protect a drug and is or may be in direct contact with it. The closure is a part of the container
Containers
Well-closed containers must protect the contents from extraneous matter or from loss of the substance under normal conditions of handling, shipment or storage.
Tightly closed containers must protect the contents from extraneous matter, from loss of the substance, and from efflorescence, deliquescence or evaporation under normal conditions of handling, shipment or storage.
Hermetically closed containers must protect the contents from extraneous matter and from loss of the substance, and be impervious to air or any other gas under normal conditions of handling, shipment or storage.

## Slide 24
Closures
Packaging closures are an important piece of the total packaging solution. All bottles, jars and even some flexible packages require a closure to seal the contents of what is inside. Closures perform a variety of functions based on the size and contents of the container they are sealing. A closure is typically used to seal a container after the initial opening in order to preserve the product for use at a later time. Closures also assist in the dispensing of the product.
Closures are devices and techniques used to close or seal container such as a bottle, jug, jar, tube, can, etc. Closures can be a cap, cover, lid, plug, etc.

## Slide 25
Depending on the contents and container, closures have several functions:
Keep the container closed and the contents contained for the specified shelf life until time of opening
Provide a barrier to dirt, oxygen, moisture, etc. Control of permeation is critical to many types of products: foods, chemicals, etc.
Keep the product secure from undesired premature opening
Provide a means of reclosing or reusing the container
Assist in dispensing and use of product
Allow reasonable ease to open the container by the intended user.

## Slide 26
Closures used for the purpose of covering drug containers after the filling process should be as inert as possible. They should not give rise to undesired interactions between the contents and the outside environment, and should provide a complete seal. Besides their protective function, closures must also allow the easy and safe administration of the drug.

## Slide 27
Depending on the type of container, closures may have different shapes and sizes, e.g. stoppers for infusion or injection bottles or plungers for prefilled syringes.
A special design of stopper may also be required for some pharmaceutical production processes such as lyophilization.
Closures, as primary packaging components, are of critical importance and must be carefully selected.
They are an essential component of the container and, as such, an integral part of the drug preparation.

## Slide 28
The following types of closures are most common in the pharmaceutical industry
Сlosure.
CT - Continuous Thread Closures: These are the most basic and commonly used packaging closure. They pair with a container that has a continuous spiral protruding on the outside of the finish or neck, as the closure itself has a thread on the inside of it. These are typically used across a number of industries including food, household items, pet products, and health & beauty.
CR or CRCs - Child Resistant Closures: These are typically used for products that are required by the Consumer Product Safety Commission to be packaged in child-resistant packaging. That means the packaging must be significantly difficult for children under five years old to open within a reasonable amount of time, while not being overly difficult for a typical adult to use properly. These are typically used for pharmaceuticals and chemical products.
TE - Tamper Evident Closures: These are used when the closure has to provide assurance that the original product is intact. These are very common in the food, beverage, and health and beauty industries. These also provide anti-counterfeiting protection for over-the-counter (OTC) pharmaceuticals and nutraceuticals.

## Slide 29
Closures are available in five basic designs:
Screw on, threaded or lug
Crimp on(crowns)
Press on(snap)
Roll on and
Friction

## Slide 30
When a screw cap is applied, its threads engaged with the corresponding threads molded on the neck of the bottle.
The liner in the cap, pressed against the opening of the container, seals the product in the container and provide the resistance to chemical and physical reaction with the product.
The screw cap is commonly made of metal or plastics. The metal is usually tin plate or aluminum and in plastic is thermoplastic and thermosetting material.
Threaded screw cap:

## Slide 31
Rubber closures
Rubber consists of several ingredients, one of which is elastomer.
Modern rubber compounds used in packaging pharmaceuticals contain only a limited number of ingredients, which are very difficult to extract. Closures made from such materials generally do not pose any problems, and can be used in contact with a large number of drug preparations.
https://www.today.com/health/child-safety-caps-do-they-really-protect-your-kids-t14111
Фильм дети

## Slide 32
https://www.youtube.com/watch?v=S-N3MrO3HtI
https://www.youtube.com/watch?v=yeKqwmuVyzE
https://www.youtube.com/watch?v=XjhqU5L4fG0
https://www.youtube.com/watch?v=Yg8-TyZd7W0
https://www.youtube.com/watch?v=bpl69Yw9H80
https://www.youtube.com/watch?v=KRgWIBfPulA