## Slide 1: Practical lesson No. 3 Theme № 3. "Pharmaco-technological properties of powdered materials."

## Slide 2
Goal. Formation of theoretical foundations in students about the physico-chemical properties of loose materials and their influence on the technology of tablet production and definition of concepts: bulk density of powders, density after shrinkage, fluidity (flowability), extrusion pressure and their influence on the technology of tablet production.
Basic concepts.
Powder - is a solid medicinal form for internal and external use, consisting of one or more solid particles of varying degrees of fineness and having the property of flowability.
Equipment: computer, multimedia equipment.

## Slide 3
The properties of the original medicinal substances largely determine the rational method of tableting. As raw materials, loose substances in the form of powder (particle size 0.2 mm) or granular (particle size from 0.2 to 3 mm) forms are used, which have the following properties:
- physical - density, shape, size and nature of the surface of particles, specific surface of particles, forces of adhesion (sticking on the surface) and cohesion (sticking of particles inside the body), surface activity, melting point, etc.;
- chemical - solubility, reactivity, etc.;
- technological — volume density, degree of compaction, flowability, moisture, fractional composition, dispersity, porosity, compactness, etc.;
- structural and mechanical - plasticity, strength, elasticity, viscosity of crystal lattices, etc.
These properties are often divided into two large groups: physical and chemical and technological.

## Slide 4
Particle shape and size. Powder medicinal substances are roughly dispersed systems and consist of particles of various shapes and sizes. Most of them are crystalline systems; the amorphous state is less common.
In many medicinal products, the particles are anisodiametric (asymmetric, multiaxial). They can be elongated, when the length significantly exceeds the transverse dimensions (sticks, needles, etc.), or lamellar, when the length and width are significantly greater than the thickness (plates, scales, tablets, leaves, etc.). A smaller part of powdery substances has isodiametric (symmetrical, equiaxed) particles — these are spherical formations, blocks, polyhedra, etc.
The shape and size of powder particles depend: in the case of crystalline substances (chemical-pharmaceutical preparations) — on the structure of the crystal lattice and the conditions of particle growth during the crystallization process, in crushed plant materials — on the anatomical and morphological features of crushed plant organs and the type of crushing machine.
The size of powder particles is determined by their length and width, which are measured using a microscope equipped with a micrometer grid, at a magnification of 400 or 600 times.

## Slide 5
The shape of the particles is determined by the ratio of the average length of the particles to the average width. With this method, particles are conditionally divided into three main types:
elongated - the ratio of length to width is more than 3 : 1;
lamellar - length exceeds width and thickness, but not more than 3 times;
equiaxed - have a spherical, polyhedral shape that is close to iso-diametric.
There are six crystal systems: cubic, hexagonal, tetragonal, rhombic, monoclinic, triclinic.
It is known that only substances belonging to the cubic system are pressed directly into tablets, that is, by direct pressing, without granulation.
Usually, powders that have the form of particles in the form of sticks are characterized by fine dispersion, good compaction and sufficient porosity (analgin, norsulfasol, acrichin, etc.).

## Slide 6
The physical properties of powders are determined by the specific and contact surface and actual density.
The specific surface area is the total surface area occupied by the powder substance, and the contact surface area is the surface area formed when the powder particles collide with each other.
The actual density of the powder is determined by the ratio of the mass of the drug to its volume at zero porosity of the powder. Any liquid that wets but does not dissolve the powder is used as a comparison. The determination is carried out using a volume meter (a pycnometer for powdered solids). The actual density (p, kg/m3) of the powder is determined by the formula:
де m — substance mass, g;
P 1— liquid density, g/cm3;
т1 — mass of volume meter with substance, g;
т2 — mass of the volume meter with liquid and substance, g.
m * P1 .
m + m1 + m2
P =

## Slide 7
For tableting, the chemical properties of the starting substances are also important, such as: the presence of water of crystallization, solubility, wettability and hygroscopicity.
Wettability. The wettability of powdered medicinal substances refers to their ability to interact with various liquids (lyophilicity) and primarily with water (hydrophilicity).
Visually, the tendency of the surface of the powders to be wetted by water is revealed:
a) complete wetting — the liquid completely spreads over the surface of the powder;
b) partial wetting — water partially spreads over the surface;
c) complete non-wetting - the drop of water does not spread, maintaining a shape close to spherical.
Hydrophobic (not wetted by water) substances can be well wetted by other liquids - for example, organic solvents.

## Slide 8
The lyophilicity of tableted powder substances is determined by the philicity coefficient, which is the ratio of the specific heat of wetting with a polar liquid (water) to the specific heat of wetting with a non-polar liquid. It is known that the formation of a monomolecular layer of wetting liquid on the surface of a solid particle is always accompanied by the release of the so-called heat of wetting.
Hygroscopicity. If the elasticity of vapors in the air is greater than their elasticity on the surface of solid particles, then the powdery mass prepared for tableting will begin to absorb steam from the air and dissolve in the absorbed water.
Crystallization water. Crystallization water molecules determine the mechanical (strength, plasticity) and thermal (dependence on the air temperature) properties of the crystal, significantly influence the behavior of the crystal under pressure.

## Slide 9
The technological properties of powdered medicinal substances depend on their physical and chemical properties.
Fractional (granulometric) composition, or the distribution of powder particles by size, affects the degree of its flowability, and therefore, the rhythmic operation of tablet machines, the stability of the weight of the received tablets, the accuracy of the dosage of the medicinal substance, as well as the quality characteristics of the tablets (appearance, disintegration, strength, etc.).
The fastest and most convenient method of determining dispersion is sieve analysis. The technique of this analysis consists in the fact that 100.0 g of the studied powder is sifted through a set of sieves (hole diameter 2.0; 1.0; 0.5; 0.25 and 0.1 mm). The weight of the material is placed on the largest (upper) sieve and the entire set of sieves is shaken (by hand or on a vibrating device) for 5 minutes, and then the mass of each fraction and its percentage content are found.

## Slide 10
It is important to determine such volume indicators of powders as bulk density, bulk volume. These indicators are determined according to the methods of the DFU (clause 2.9.15).
During tableting, the most important technological properties are fluidity, compressibility and sliding, which allows you to easily push the tablet out of the matrix.
Fluidity (flowability) is the ability of the powder system to pour out of the funnel or "flow" under the influence of its own weight and ensure uniform filling of the matrix channel.
The same method also determines the angle of natural slope - the angle between the origin of the cone of loose material and the horizontal plane. The angle of the natural slope varies widely — from 25 to 30° for well-flowing materials and 60-70° for bound materials.
The fluidity of powders is a complex characteristic determined by the dispersion and shape of the particles, the moisture content of the masses, and the granulometric composition. This technological characteristic can be used when choosing tableting technology.

## Slide 11
Compressibility is the ability of powder particles to be cohesive under pressure, i.e., the ability of particles under the influence of electromagnetic forces (molecular, adsorption, electrical) and mechanical engagement to attract each other and bond with the formation of a stable, strong compressed product.
Compressibility is characterized by the strength of the model tablet after the pressure is removed. The better the compressibility of the powder, the higher the strength of the tablet. If the compressibility is poor, the tablet is formed weakly, and sometimes completely collapses when pushed out of the matrix.
When determining the compressibility of the powder (granules), a weight of 0.3 or 0.5 g is pressed in a matrix using punches with a diameter of 9 mm and 11 mm on a hydraulic press at a pressure of 120 MPa. The resulting tablet is weighed on a torsion balance, the height is measured with a micrometer, and the compressibility factor (Ks, g/mm) is calculated according to the formula:
де: m — tablet mass, g;
h — tablet height, mm.
Ks =
m
h

## Slide 12
The force of pushing tablets out of the matrix. To push the pressed tablet out of the matrix, you need to apply force to overcome the friction and adhesion between the side surface of the tablet and the wall of the matrix. Taking into account the magnitude of the push-out force, the addition of anti-friction (sliding or lubricating) substances is predicted.
Calculation of the pushing force is carried out according to the formula:
де Рвишт— ejection pressure, MPa;
Рман — pressure gauge reading, MPa;
Snji— plunger area, m2;
S6i4—area of the side surface of the tablet, m

## Slide 13
The area of the side surface of the tablet is calculated according to the formula:
де г — tablet radius, m;
h — tablet height, m
Nature of connection of particles in tablets. Tableting is based on the use of the properties of powdered medicinal substances to compact and solidify under pressure. At the same time, the weakly structured material turns into a cohesive dispersion system with a certain amount of porosity. In many respects, such a system is close in its properties to a compact body in which certain adhesion forces act.

## Slide 14
Tests
1. According to the method of production, tablets are divided into two classes:
A pressed and molded tablets,
B molded and effervescent,
C tablets with a shell and a film,
D enteric and effervescent,
E for oral and vaginal.
2. The sizes of tablets in diameter range from ...
A 4 to 25 mm,
B 2 to 14 mm,
C 5 to 40 mm,
D 10 to 50 mm.
3. The true density of the powder is determined by the ratio …..
A of the mass of the drug to its volume, with zero porosity of the powder,
B of the volume of the drug to its density,
C mass of the drug to its moisture content,
D concentration of the drug to its volume, with zero porosity of the powder.
E -.

## Slide 15
4. The following chemical properties are important for tableting, namely:
A presence of water of crystallization, solubility, wettability and hygroscopicity,
B the presence of impurities, solubility, irrigability and flowability,
C presence of hygroscopicity and homogeneity of particles,
D presence of good solubility and wettability.
5. Bulk density is:
A is the mass of a unit volume of freely poured powder, which depends on the density of the substance, the shape and size of the particles, their stacking,
B is the mass of a unit volume of freely poured powder, which depends on the moisture content of the substance, the shape and their stacking,
C is the volume of the free space between the powder particles,
D is the ratio of bulk density to true density.
E-.
6. The volume of free space (pores, voids) between powder particles:
A Porosity,
B Bulk density,
C Relative density,
D Raw material moisture,
E Fractional composition

## Slide 16
7. Knowing which value allows you to predict the standard sizes of tablets, to correctly choose the amount of pressing pressure for obtaining tablets.
A Flowability of the substance;
B Bulk density,
C Fractional composition,
D Porosity,
E -.
8. The shape, size and nature of the surface of the powder particles are determined using...
A Microscope,
B Dandruff,
C Telescope,
D Without devices,
E -.
9. The true density of the powder is determined using ....
A Volume meter,
B Microscope,
C pH meter,
D spectrophotometer,
E –
10. Relative density (ton, %) is calculated as:
A Percentage ratio of bulk (bulk) density to true density,
B percentage ratio of humidity to true density,
C is the percentage ratio of bulk (bulk) density to grinding.
D is the percentage ratio of bulk density to concentration.
E -

## Slide 17
Questions for self-control:
1. Physico-chemical properties of powdered materials.
2. Technological volume density, degree of compaction, flowability of powdered materials.
3. Moisture, fractional composition of powdered materials.
4. Dispersity, compressibility of powdered materials.
5. Structural and mechanical properties: plasticity, strength, elasticity, viscosity of the crystal lattice, etc.
6. Determination of the shape, size and nature of the powder surface, determination of moisture content.
7. Setting fractional composition, bulk density, true density, relative density.
8. Determination of porosity, flowability, compressibility, etc.

## Slide 18
Basic literature:
1. Gladukh E.V. Theoretical foundations of pharmaceutical technology. Study guide for extracurricular independent work / E.V. Gladukh, I.V. Saiko, A.A. Sichkar, D.P. Soldatov. Kh.: NFaU, 2016. - 202 p.
2. Technology of drugs of industrial production (vol. 2 of 2). Chuyeshov V. I., Gladukh E. V., Saiko I. V., Lyapunova O. O., Sichkar A. A., Krutskikh T. V., Ruban O. A. Kh.: National University of Applied Sciences; Golden Pages, 2013. - 638 p.
3. Technology of drugs of industrial production (vol. 1 of 2). Chuyeshov V. I., Gladukh E. V., Saiko I. V., Lyapunova O. O., Sichkar A. A., Krutskikh T. V., Ruban O. A. Kh.: National University of Applied Sciences; Golden Pages, 2012. - 694 p.
List of recommended literature (main, additional, electronic information resources):

## Slide 19
Additional literature:
1. Technological equipment of the pharmaceutical and biotechnological industry: tutorial. for university students education closing III-IV accreditation level / M.V. Stasevych and others; 2nd ed., revision. and added – Lviv: Novy svit-2000, 2018. – 410 p.
2. Yarnykh, T. G. Extemporaneous formulation (technology, analysis, application): method. rec. / T. G. Yarnykh, Fr. I. Tikhonov, I. S. Hryshchenko and others. - Kh., 2015. -379 p.
3. State Pharmacopoeia of Ukraine / State enterprise "Ukrainian Scientific Pharmacopoeia Center for the Quality of Medicinal Products" - 2nd edition. - Kharkiv: State Enterprise "Ukrainian Scientific Pharmacopoeia Center for the Quality of Medicinal Products", 2015. - Vol. 1. -1128 p.
4. Extraction of plant raw materials: training. Guide / Yu. I. Sidorov, I. I. Gubytska, R. T. Konechna, V. P. Novikov. – Lviv: View of the National Lviv Polytechnic University, 2018. - 336 p.
5. History of medicine and pharmacy: teaching. manual for pharmacy students. education closing and pharmacy Faculty of Higher Education of the Ministry of Health of Ukraine / A. A. Kotvitska, V. V. Gorbanev, O. O. Surikov and others. – Kharkiv: National Institute of Economics and Technology: Golden Pages, 2016. – 168 p.

## Slide 20
Thank you for attention!