## Slide 1: Practical lesson No. 4 Тheme № 4 «Theoretical foundations of grinding of solid bodies. Theories of crushing of solid bodies».

## Slide 2
Goal. Students' formation of theoretical foundations about grinding, classes of grinding, degree of grinding and methods of grinding. To learn the theoretical basics of grinding solid bodies.
Basic concepts. Splitting - the body breaks into particles in the places of concentration of the greatest loads, which arise as a result of the action of wedge-shaped working elements. The method of splitting in comparison with crushing allows you to adjust the size of the obtained particles.
Breaking - the body is destroyed under the action of bending forces. The size and shape of the particles obtained by breaking are approximately the same as by splitting.
Cutting - the body is divided into particles of predetermined sizes and shapes.
Abrasion - the body is crushed under the action of compressive, stretching and shearing forces. At the same time, a fine dust-like product is obtained.
Impact - the body is destroyed into particles under the action of a dynamic load. There is a difference between compressed and free stroke.
Equipment: computer, multimedia equipment.

## Slide 3
The intensity of physical and chemical processes involving the solid phase increases with an increase in the surface of a solid material, which is achieved by reducing its size. In this regard, various solid materials are subjected to mechanical grinding in many chemical industries, which is of great importance in the manufacture of dosage forms.
Grinding is the process of reducing the size of material particles by destroying them under the action of external forces that overcome the internal forces of adhesion that bind the particles of a solid substance together.
The characteristics of the crushed material are the following parameters: dispersion (fractional, granulometric composition), passage D (residue R), fraction ΔD or ΔR.

## Slide 4
To determine the complete picture of the fractional composition of the crushed material, distribution functions are used, which represent the dependence of the passage D or the residue R on the diameter (size) of the particles.
One of the characteristics of the material is the specific surface, that is, the surface of the particles, which refers to a unit of mass or volume of the material.
Average particle diameter, median diameter, and others are used as conventional indicators.
The material can also be characterized by the permissible percentage content of a certain fraction: large, medium and small.
Grinding methods mean the kind of impact on a solid material that leads to its destruction.

## Slide 5
Solid material can be destroyed by the following grinding methods: crushing, splitting, breaking, cutting, sawing, abrasion, impact and various combinations of these methods.
Crushing is a type of failure in which the deforming load acting on the body leads to an increase in internal stress above the compressive strength limit.
As a result of such destruction, particles of different sizes and shapes are obtained.
Splitting - the body breaks into particles in the places of concentration of the greatest loads, which arise as a result of the action of wedge-shaped working elements. The method of splitting in comparison with crushing allows you to adjust the size of the obtained particles.

## Slide 6
Breaking - the body is destroyed under the action of bending forces. The size and shape of the particles obtained by breaking are approximately the same as by splitting.
Cutting - the body is divided into particles of predetermined sizes and shapes.
Abrasion - the body is crushed under the action of compressive, stretching and shearing forces. At the same time, a fine dust-like product is obtained.
Impact - the body is destroyed into particles under the action of a dynamic load. There is a difference between compressed and free stroke.
With a compressed impact, the body is destroyed between two working bodies of the shredder. The effect of such destruction depends on the kinetic energy of the impacting body.

## Slide 7
With a free impact, the destruction of the body occurs as a result of its collision with the working body of the shredder or other bodies in flight. The effect of such destruction is determined by the speed of their collision, regardless of whether the body that is destroyed or the working body of the shredder moves. In most cases, these types of influence on the material are used in combination, while most often only one of them is decisive.
Depending on the physical and mechanical properties, particle sizes of the starting material and the final product, one or another method of grinding is chosen, while it is also necessary to take into account the moisture content of the material and other properties.

## Slide 8
1. The process of reducing the size of material particles by destroying them under the action of external forces that overcome the internal forces of adhesion that connect the particles of a solid substance is called:
A grinding,
B dissolution,
C dispersion,
D extraction,
E solution.
2. The ratio of the particle sizes of the original and crushed material is called...
A degree of grinding,
B solubility,
C concentration,
D dispersion.
Tests

## Slide 9
3. According to the Mohs hardness scale, quartz …..
A scratches the glass,
B scratches with his fingernail,
C cuts glass,
D has the hardness of window glass.
E -.
4. The strength limit (10-5 N/m2) of quartz is:
A 1200-1500,
B 1450,
C 300-1500,
D 1000-2500.
5. How to grind a viscous, medium-hard material:
A abrasion with impact,
B crushing, impact,
C splitting, abrasion,
D crushing.
E-.
6. According to the surface theory (Rittinger theory)…
A the useful work of grinding is spent on the formation of new surfaces,
B the useful work of abrasion is spent on reducing the formation of new surfaces.
C useful work of grinding is spent on volumetric deformation of particles that are destroyed,
D useful grinding work is spent on the partial deformation of the particles.
E -

## Slide 10
7. What is the name of the theory that shows that the useful work of grinding is spent on the volumetric deformation of the particles that are destroyed.
A Volumetric theory (Kirpychov-Kick theory),
B Surface theory (Rittinger theory),
C Rebinder's theory,
D Benedict's theory.
E -.

## Slide 11
3.1. Tasks for fixing the material
№№ c.e. | Mein Tasks | Instruction’s | Answers
1 | 2 | 3 | 4
1. | Grinding classes. | your answers | 
2. | Shredding by crushing and splitting. | your answers | 
3. | Shredding by breaking and cutting. | your answers | 
4. | The method of grinding according to the Mohs scale. | your answers | 
5. | Strength limit and modulus of elasticity of materials. | your answers | 
6. | Groups of materials depending on strength. | your answers | 
7. | Grinding methods depending on the type of material. | your answers | 
8. | Gates of Energy | your answers | 
9. | Surface theory (Rittinger's theory). | your answers | 
10. | Bulk theory (Kirpychov-Kick theory). | your answers | 

## Slide 12
3.2. Questions for self-control:
1. Grinding. Grinding classes, degree of grinding.
2. Methods of grinding (crushing, splitting, breaking, cutting).
3. Mohs hardness scale.
4. Strength limit and modulus of elasticity of some materials.
5. Groups of materials depending on strength.
6. Grinding methods depending on the type of material.
7. Physico-mechanical basics of grinding.
8. Energy consumption.
9. Stages and main grinding schemes.
10. Classification of shredders.
11. Comparison and selection of shredders.

## Slide 13
Basic literature:
1. Gladukh E.V. Theoretical foundations of pharmaceutical technology. Study guide for extracurricular independent work / E.V. Gladukh, I.V. Saiko, A.A. Sichkar, D.P. Soldatov. Kh.: NFaU, 2016. - 202 p.
2. Technology of drugs of industrial production (vol. 2 of 2). Chuyeshov V. I., Gladukh E. V., Saiko I. V., Lyapunova O. O., Sichkar A. A., Krutskikh T. V., Ruban O. A. Kh.: National University of Applied Sciences; Golden Pages, 2013. - 638 p.
3. Technology of drugs of industrial production (vol. 1 of 2). Chuyeshov V. I., Gladukh E. V., Saiko I. V., Lyapunova O. O., Sichkar A. A., Krutskikh T. V., Ruban O. A. Kh.: National University of Applied Sciences; Golden Pages, 2012. - 694 p.
List of recommended literature (main, additional, electronic information resources):

## Slide 14
Additional literature:
1. Technological equipment of the pharmaceutical and biotechnological industry: tutorial. for university students education closing III-IV accreditation level / M.V. Stasevych and others; 2nd ed., revision. and added – Lviv: Novy svit-2000, 2018. – 410 p.
2. Yarnykh, T. G. Extemporaneous formulation (technology, analysis, application): method. rec. / T. G. Yarnykh, Fr. I. Tikhonov, I. S. Hryshchenko and others. - Kh., 2015. -379 p.
3. State Pharmacopoeia of Ukraine / State enterprise "Ukrainian Scientific Pharmacopoeia Center for the Quality of Medicinal Products" - 2nd edition. - Kharkiv: State Enterprise "Ukrainian Scientific Pharmacopoeia Center for the Quality of Medicinal Products", 2015. - Vol. 1. -1128 p.
4. Extraction of plant raw materials: training. Guide / Yu. I. Sidorov, I. I. Gubytska, R. T. Konechna, V. P. Novikov. – Lviv: View of the National Lviv Polytechnic University, 2018. - 336 p.
5. History of medicine and pharmacy: teaching. manual for pharmacy students. education closing and pharmacy Faculty of Higher Education of the Ministry of Health of Ukraine / A. A. Kotvitska, V. V. Gorbanev, O. O. Surikov and others. – Kharkiv: National Institute of Economics and Technology: Golden Pages, 2016. – 168 p.

## Slide 15
Thank you for attention!