## Slide 1: Practical lesson No. 5 Тheme № 5 «Methods of determining the size of particles of solid bodies. Sifting and mixing of powdered materials. Theoretical foundations of pressing».

## Slide 2
Goal. Formation of theoretical foundations for students about the main stages and features of sieving and mixing of solids with subsequent production of medicinal forms.
Basic concepts. Sifting – is the process of obtaining a product with the same particle size. Sifting is regulated according to the State Federal Office of Internal Affairs and Communications I.
Mixing – is a mandatory operation in the manufacture of powders. It can be carried out simultaneously with powdering or independently, if a complex powder is prepared from an already crushed substance. In pharmacies, powders are mixed mainly in a mortar. This operation should be carried out with frequent collection of powder from the walls of the mortar and pestle to the center of the mortar with the help of a celluloid capsule.
Equipment: computer, multimedia equipment.

## Slide 3
An important point in the production of powders is familiarization with the main operations and equipment necessary for the production of powders; to study the peculiarities of the technology of solid dosage forms. Peculiarities of sieving and mixing of powdered materials.
Depending on the medical purpose and the method of application, powders have different requirements for dispersion. Crystalline powders intended for dissolution before use by patients (magnesium sulfate, boric acid, etc.) are usually produced in the form of powders with a particle size of 0.2 to 0.3 mm. Powder powders intended for the treatment of various injuries of the skin or mucous membranes must be ground very finely (0.090-0.093 mm) in order to increase the total surface of the particles of these substances and reduce their traumatic effect.

## Slide 4
When obtaining complex powders in industrial conditions, each substance included in the composition of the mixture is crushed separately and sifted through a suitable sieve. When sieving mixtures through the holes of the sieves, first of all, particles that are smaller and have a higher specific mass pass through. Then lighter and larger particles are sifted out. As a result of this, the screening is arranged in layers of different quality. Therefore, after sifting, the materials must be thoroughly mixed again.

## Slide 5
In industrial conditions, mechanical designs of sieves are used: rotating, oscillating, vibrating. According to the construction of vibrating devices, there are 3 types of vibrating sieves: electromagnetic, gyrational, inertial.
Sifting of crushed material is carried out with the help of sieve mechanisms of various designs: rotating, swinging and vibrating. Wet material can be sifted on vibrating sieves.

## Slide 6
Mixing of powdered products is carried out in special mixers, which are classified as:
- by the nature of the mixing process (convection or diffusion),
- a design feature (drum mixers with a rotating body and rotating blades),
- by the method of action on the mixture (gravitational, centrifugal),
- the nature of the mixing process (periodic or continuous) and other features.

## Slide 7
A qualitative characteristic of the mixing process is the homogeneity of the composition of any of the samples taken from different zones of the mixer.
The mixing process is influenced by the following factors: surface forces (electrostatic, molecular, van der Waals), shape and size of particles and their density. The time of mixing simple and complex prescriptions in the dry state is from 3 to 12 min., and in the moistened state - from 5 to 20 min. To obtain a homogeneous mixture of bulk materials, fluidized bed mixers are used. The basic principle of mixing is that a smaller quantity is added to a larger quantity in order to avoid the loss of small quantities of substances.

## Slide 8
The simplest and easiest method of mixing is one in which the ingredients are part of the powder in approximately equal quantities, with particles of the same size and close in density. All components are poured into a mixer and mixed until a homogeneous mixture is obtained. If, under the specified equal conditions, the specific mass of the mixed powders is different, then the duration of mixing increases. If a small amount of a poisonous or potent substance or essential oil needs to be added to a large amount of substances, then they must first be thoroughly mixed with one of the ingredients or with an indifferent powdery substance. In some cases, substances that are part of the mixture in small quantities, it is better to dissolve in a small amount of solvent.

## Slide 9
Tests
1. Grinding machines are classified according to the method of grinding the material into:
A. disc, ball, rotary machines;
B. disk, cutting, fine grinding machines;
C. crushers for medium, fine, colloidal, fine grinding;
D. cutting, grinding, crushing, impact, impact-centrifugal machines;
E. grass cutters, root cutters.
2. When determining the technological properties of powders, flowability is determined. What devices are used to determine this indicator?
A. vibrating watering can;
B. disintegrator;
C. dismembranator;
D. set of sieves;
E. friabilator.

## Slide 10
3. At pharmaceutical enterprises, in the production of powders, the operation of grinding medicinal substances is used. What machines are used for fine grinding of substances:
A. dismebrators;
B. drum mills, vibrating mills;
C. grass and root cutters;
D. roll shredders;
E. disintegrators.
4. The pharmaceutical enterprise produces powders for various purposes. Specify the degree of grinding of the powders given in the DFU:
A. large, medium, thin;
B. large, medium-large, medium-small, small, smaller, smallest;
C. large, medium-large, medium-fine, smaller, colloidal;
D. large, medium, small, colloidal;
E. large, medium, small, smallest.

## Slide 11
5. Grinding equipment is classified by the method of grinding. What machines does a roller crusher include:
A. percussion;
B. erasing;
C. crushing;
D. cutting;
E. shock-centrifugal
6. Mixers are used to obtain a homogeneous mixture of loose materials. Which faucets do not have rotating parts:
A. double-cone mixers;
B. drum mixers;
C. blade mixers;
D. fluidized bed mixers;
E. centrifugal mixers.

## Slide 12
7. Knowing which value allows you to predict the standard sizes of tablets, to correctly choose the amount of pressing pressure for obtaining tablets.
A Flowability of the substance;
B Bulk density,
C Fractional composition,
D Porosity,
E -.
8. The shape, size and nature of the surface of the powder particles are determined using...
A Microscope,
B Dandruff,
C Telescope,
D Without devices,
E -.

## Slide 13
9. The true density of the powder is determined using ....
A Volume meter,
B Microscope,
C pH meter,
D spectrophotometer,
E –

## Slide 14
3.1. Tasks for fixing the material
№№ c.e. | Mein Tasks | Instructions | Answers
1 | 2 | 3 | 4
1. | What is shredding? | your answer | 
2. | Name the main requirements when grinding a substance. | your answer | 
3. | What equipment is used for the grinding process? | your answer | 
4. | Describe the sieving process. | your answer | 
5. | Name the main types and principle of operation of industrial sieves. | your answer | 
6. | Describe the mixing process. | your answer | 
7. | Name the main technological characteristics used in the mixing process. | your answer | 
8. | Name the equipment used in the mixing process. | your answer | 
9. | Describe the granulation process and stages | your answer | 
10. | Name the main stages of pressing. | your answer | 

## Slide 15
3.2. Questions for self-control:
1. Methods of determining the size of particles of solid bodies.
2. Mechanical processes.
3. Shredding of solid materials.
4. Classification and sorting of materials.
5. Mixing solid materials.
6. Drum, screw and blade mixers.
7. Theoretical foundations of pressing.
8. Features of pressing and main stages.

## Slide 16
Basic literature:
1. Gladukh E.V. Theoretical foundations of pharmaceutical technology. Study guide for extracurricular independent work / E.V. Gladukh, I.V. Saiko, A.A. Sichkar, D.P. Soldatov. Kh.: NFaU, 2016. - 202 p.
2. Technology of drugs of industrial production (vol. 2 of 2). Chuyeshov V. I., Gladukh E. V., Saiko I. V., Lyapunova O. O., Sichkar A. A., Krutskikh T. V., Ruban O. A. Kh.: National University of Applied Sciences; Golden Pages, 2013. - 638 p.
3. Technology of drugs of industrial production (vol. 1 of 2). Chuyeshov V. I., Gladukh E. V., Saiko I. V., Lyapunova O. O., Sichkar A. A., Krutskikh T. V., Ruban O. A. Kh.: National University of Applied Sciences; Golden Pages, 2012. - 694 p.
List of recommended literature (main, additional, electronic information resources):

## Slide 17
Additional literature:
1. Technological equipment of the pharmaceutical and biotechnological industry: tutorial. for university students education closing III-IV accreditation level / M.V. Stasevych and others; 2nd ed., revision. and added – Lviv: Novy svit-2000, 2018. – 410 p.
2. Yarnykh, T. G. Extemporaneous formulation (technology, analysis, application): method. rec. / T. G. Yarnykh, Fr. I. Tikhonov, I. S. Hryshchenko and others. - Kh., 2015. -379 p.
3. State Pharmacopoeia of Ukraine / State enterprise "Ukrainian Scientific Pharmacopoeia Center for the Quality of Medicinal Products" - 2nd edition. - Kharkiv: State Enterprise "Ukrainian Scientific Pharmacopoeia Center for the Quality of Medicinal Products", 2015. - Vol. 1. -1128 p.
4. Extraction of plant raw materials: training. Guide / Yu. I. Sidorov, I. I. Gubytska, R. T. Konechna, V. P. Novikov. – Lviv: View of the National Lviv Polytechnic University, 2018. - 336 p.
5. History of medicine and pharmacy: teaching. manual for pharmacy students. education closing and pharmacy Faculty of Higher Education of the Ministry of Health of Ukraine / A. A. Kotvitska, V. V. Gorbanev, O. O. Surikov and others. – Kharkiv: National Institute of Economics and Technology: Golden Pages, 2016. – 168 p.

## Slide 18
Thank you for attention!