## Slide 1: Practical lesson No. 7 Theme № 7. "Classification of emulsifiers. Properties of surfactants (surfactants). Classification of surfatants and their purpose."

## Slide 2
Goal. The formation of students' theoretical knowledge about the physicochemical properties of emulsifiers, their structural formulas, the main requirements that emulsifiers must meet and their classification. To learn the physical and chemical properties of emulsifiers, their classification and main characteristics.
Basic concepts.
Surface-active substances (surfactants) – are a huge group of substances that cause a decrease in surface tension at the interface of the phases of substances that do not dissolve in each other. Simply put, dirt is washed off thanks to surface-active substances.

## Slide 3
Solubilization - is the improvement of solubility with the help of surfactants, which are able to convert poorly soluble or completely insoluble substances into transparent or, in extreme cases, into opalescent solutions without changing their chemical structure.
Cationic emulsifiers – are surfactants that form organic cations in an aqueous solution.
Anionic emulsifiers – are surfactants that are dissociated in an aqueous solution.
Nonionic emulsifiers – are surfactants that do not form ions in an aqueous environment, so they have certain advantages over ionic emulsifiers.
Equipment: computer, multimedia equipment.

## Slide 4
One of the most important components of dispersed systems of medicinal products are surfactants (surfactants). Due to their wide use, these means have remarkable preventive and curative properties and are in great demand among the population. Most of the creams for external use are created on the basis of emulsions. The use of emulsion forms is due to their specific properties, such as the ability to combine oil and water phases, the possibility of introducing various active components, as well as good consumer properties, such as moisturizing ability, easy absorption and easy application to the skin.

## Slide 5
One of the most important components of dispersed systems of cosmetic preparations is surfactants (surfactants). They are unevenly distributed in the solution, and due to their amphiphilic (hydrophilic-hydrophobic) character, they are concentrated (adsorbed) on the surfaces of phase separation, forming adsorption layers. The result of this process is a decrease in interfacial tension. Surfactant molecules contain lipophilic (hydrophobic) and hydrophilic functional groups.
In principle, all emulsifiers can be considered surfactants.

## Slide 6
Surfactants are emulsifiers that are used in the manufacture of pharmaceutical products and perform special tasks, therefore they must meet the following specific requirements:
- toxicological safety;
- high biological degradation;
- confirmed compatibility with human skin and mucous membranes;
guaranteed status of admission to use: having a passport and inclusion in the pharmacopoeia or registration in INCI and the like.

## Slide 7
It is also advisable to fulfill a number of other conditions, such as multifunctionality (for example, obtaining an additional cosmetic effect), as well as to achieve such important advantages as the possibility of using an emulsifier in a low concentration, which leads to energy savings.

## Slide 8
Physico-chemical properties of surfactants and emulsifiers
Aggregation. After reaching a certain concentration, surfactant molecules are able to form relatively large molecular aggregates - micelles. This concentration characteristic of each surfactant is called the critical micelle formation concentration (CMC). This process is reversed: when the solution is diluted with a solvent below the CCM, the surfactant micelles again break down into individual molecules (monomers). Thermodynamic equilibrium is established between monomers and micelles, and it does not matter where the surfactant monomer molecules are located - at the boundary of the phase separation or in the volume of the solution.

## Slide 9
Monomers in the micelle are placed so that their hydrophobic groups are inside, they are not in direct contact with the solvent, and hydrophilic groups are distributed on the surface of the micelle and ensure their stability in solution
Micelles can have different shapes and sizes. The number of monomers in the micelle fluctuates around the average value characteristic of each surfactant. Nonionic, low molecular weight surfactants have an aggregation number of the order of 50–1000; and in anionic, cationic - charged ones, it is about 50. This is explained by the fact that the electrostatic repulsion between equally charged groups does not create conditions for further aggregation. In addition to spherical, thermodynamically stable forms of aggregation can also be called ellipsoids, paliceta, disk-shaped micelles.

## Slide 10
The macroscopic properties of solutions containing surfactants, especially their viscosity, depend on the size and shape of the aggregates. For many applications, especially in cosmetics, this is as important as the fact that molecules dispersed in solution have only a slight solubility or even no solubility at all. They can only be mounted inside the micelle and thereby transferred into the solution. This process is called solubilization, or colloidal solubility.

## Slide 11
Solubilization should be understood as the improvement of solubility with the help of surfactants, which are able to convert poorly soluble or completely insoluble substances into transparent or, in the extreme case, into opalescent solutions without changing their chemical structure. For solubilization, mainly surfactants with a low value of CCM and so that they are indifferent to chemical interactions are used.
Emulsifiers with two long hydrocarbon chains in the process of their aggregation form another structure that distinguishes them from emulsifiers with one hydrocarbon radical. They spontaneously form multi-layered empty balls - vesicles.

## Slide 12
Liposomes are spherical vesicles (25–5000 nm in diameter), the membranes of which consist of one or more double layers of amphiphilic lecithin molecules. At the same time, the lipophilic (hydrophobic) parts of the surfactant are always directed towards the middle of the double layer. If the vesicles form nonionic emulsifiers, they are called niosomes. Thus, the inner core of liposomes and niosomes always forms a water phase.
Due to their characteristic structure, vesicles are potential delivery systems for hydrophilic systems and water in the stratum corneum or are carriers of lipophilic and amphiphilic molecules (in lipophilic membranes).

## Slide 13
Classification of emulsifiers:
Anionic emulsifiers are dissociated in aqueous solution. The anion is responsible for the emulsifying effect, but the counterion also determines the technological properties. Fatty acid soap (С12–С18) is an important emulsifier in cosmetic products. Clarification: only water-soluble or colloidally dispersed sodium, potassium, ammonium, or amine salts are called soaps, while water-insoluble calcium, magnesium, zinc, and aluminum salts are called metal soaps."
From a chemical point of view, soaps mean alkali metal salts of fatty acids, which are formed after the neutralization of fatty acids with alkali. The chemical structures of fatty acid soaps and sodium stearyl sulfate are shown in Fig. 17.
The use of sodium hydroxide solution gives mainly solid soaps, potassium hydroxide - from liquid to pasty. Due to their low viscosity, they are also called liquid soaps.
The cleansing action of amphiphilic salts of fatty acids consists in the fact that their solutions wet the surface of the skin, disperse, emulsify or solubilize particles of pollution stuck to the surface, and then transfer them into a solution.

## Slide 14
Cationic emulsifiers form organic cations in an aqueous solution.
Due to their ionic character, they are very hydrophilic. Unlike anionic emulsifiers, they have strong preservative properties, so special attention should be paid to dermatological compatibility.
The use of cationic emulsifiers in emulsions is limited by their possible interaction with anionic compounds, and this can reduce their emulsifying ability. Emulsions based on cationic emulsifiers are easily destroyed on the skin, which is explained by a strong interaction with the skin surface. The high adsorption capacity is due to the electrostatic attraction between the opposite charges of the skin surface and the cation of the emulsifier. In this case, the hydrophobic residues of their molecule are directed to the outer side of the skin. As a result, a hydrophobized skin surface is formed; it seems elastic and soft.

## Slide 15
Ampholyte emulsifiers combine both types of ions in one molecule. Their most important representatives are lecithins and phospholipids. Both of them belong to the group of phosphatides, because they consist of residues of phosphoric acid, fatty acids, alcohol and a nitrogenous component.
Lecithin is produced from egg yolks or from plants - soybeans. The composition of fatty acids it contains greatly affects its technological properties. Phospholipids as natural surfactants are able to stabilize emulsions of various types and can be auxiliary dispersants in suspensions. They are able to form vesicles in the form of liposomes, and in higher concentrations - lamellar liquid crystal phases. These phases are very stable and have sufficient variation in water and fat content. Recipes with lecithin differ from others in their special stability.
This makes it possible to formulate formulations of emulsions and creams, which, depending on the amount of water, will have a lipophilic or hydrophilic character. In addition, phospholipids are non-toxic, do not cause allergies and irritation. The ability to bind and hold water can make them humectants.

## Slide 16
Nonionic emulsifiers do not form ions in an aqueous environment, so they have certain advantages over ionic emulsifiers. Electrolytes do not affect their properties, and they behave too indifferently to chemical interactions in recipes. The simplest representatives of substances of this class are higher fatty alcohols, stearins and incomplete esters of fatty acids and polyatomic alcohols. All these substances have in common that the share of their hydrophilic groups in their molecules is very small (one or more hydroxyls), so they are lipophilic fat-soluble substances.

## Slide 17
Тests
1. All surface-active substances are concentrated on the surfaces of phase separation, forming adsorption layers. What is it connected with?
A due to amphiphilic properties,
B due to hydrophilic properties,
C due to hydrophobic properties,
D due to the absence of a lipophilic group,
E -.
2. Molecules of surface-active substances contain in their composition...
A lipophilic and hydrophilic functional groups.
B exclusively only a lipophilic group.
C exclusively hydrophilic group.
D ten hydrophobic groups.

## Slide 18
3. Macroscopic properties of solutions containing surfactants, especially their viscosity, depends on the size and shape of the aggregates, their molecules are distributed in the solution, have only a slight solubility or even do not dissolve at all. This process is called…
A solubilization,
B hydrophilicity,
C lipophilicity,
D amphiphilic properties.
E -.
4. For solubilization, mainly surfactants are used, indicators of the critical concentration of micelle formation, which have...
A low values,
B high values,
C presence of hygroscopicity and homogeneity of particles,
D presence of good solubility and wettability.

## Slide 19
5. Which emulsifiers in the process of their aggregation form multi-layered empty balls - vesicles?
A with two long hydrocarbon chains,
B with three short hydrocarbon chains,
C with one long hydrocarbon chain,
D with four short hydrocarbon chains.
E-.
6. Liposomes are spherical vesicles whose membranes consist of...
A of several double layers of amphiphilic lecithin molecules,
B of several double layers of hydrophobic structures,
C of one layer of lecithin,
D three layers of fat,
E fractional sklaud.

## Slide 20
7. What are the vesicles that form nonionic emulsifiers called?
A by niosomes;
B polysomes,
C trichosomes,
D sometimes
E -.
8. The most important representatives of ampholytic emulsifiers are...
A lecithins and phospholipids,
B fatty alcohols,
C stearins and unsaturated fatty acid esters,
D polyhydric alcohols,
E -.

## Slide 21
9. Cationic emulsifiers form in an aqueous solution...
A organic cations,
B organic anions,
C salts,
D alcohols,
E -
10. The use of cationic emulsifiers in emulsions is limited by their possible interaction with anionic compounds, and this can lead to ....
A decrease in their emulsifying ability,
B increasing their emulsifying ability,
C neutralization of their emulsifying ability,
D formation of salts.
E –

## Slide 22
3.1. Tasks for fixing the material
№№ c.e. | Mein tasks | Instructions | Answers
1 | 2 | 3 | 4
1. | Define the concept of emulsifiers? | your answer | 
2. | The main criteria of emulsifiers? | your answer | 
3. | Physico-chemical properties of surfactants and emulsifiers. | your answer | 
4. | Anionic emulsifiers. | your answer | 
5. | Cationic emulsifiers. | your answer | 
6. | Ampholytic emulsifiers. | your answer | 
7. | Nonionic emulsifiers. | your answer | 
8. | Polymeric emulsifiers. | your answer | 
9. | Emulsions as liquid systems. | your answer | 
10. | Surfactants (surfactants) | your answer | 

## Slide 23
3.2. Questions for self-control:
1. Surfactant emulsifiers used in the manufacture of dosage forms. Give examples.
2. Describe the physical and chemical properties of surfactants.
3. What is solubilization?
4. What is the significance of solubilization in the process of dissolving insoluble substances?
4. What are vesicular systems? Mesophases.
5. Name anionic emulsifiers. Examples.
6. Cationic and ampholyte emulsifiers. Lecithin. Appointment.
7. Describe nonionic emulsifiers. What is lanolin?
8. Nonionic emulsifiers based on sugars and polyglycerols. Give examples.
9. System of hydrophilic-lipophilic balance of nonionic surfactants.
10. Polymer emulsifiers. The principle of their action.
11. Surface-active substances in cosmetics, anionic surfactants. Give examples of their use.
12. Nonionic surfactants, amphoteric and cationic surfactants. The principle of their action and use.

## Slide 24
Basic literature:
1. Gladukh E.V. Theoretical foundations of pharmaceutical technology. Study guide for extracurricular independent work / E.V. Gladukh, I.V. Saiko, A.A. Sichkar, D.P. Soldatov. Kh.: NFaU, 2016. - 202 p.
2. Technology of drugs of industrial production (vol. 2 of 2). Chuyeshov V. I., Gladukh E. V., Saiko I. V., Lyapunova O. O., Sichkar A. A., Krutskikh T. V., Ruban O. A. Kh.: National University of Applied Sciences; Golden Pages, 2013. - 638 p.
3. Technology of drugs of industrial production (vol. 1 of 2). Chuyeshov V. I., Gladukh E. V., Saiko I. V., Lyapunova O. O., Sichkar A. A., Krutskikh T. V., Ruban O. A. Kh.: National University of Applied Sciences; Golden Pages, 2012. - 694 p.
List of recommended literature (main, additional, electronic information resources):

## Slide 25
Additional literature:
1. Technological equipment of the pharmaceutical and biotechnological industry: tutorial. for university students education closing III-IV accreditation level / M.V. Stasevych and others; 2nd ed., revision. and added – Lviv: Novy svit-2000, 2018. – 410 p.
2. Yarnykh, T. G. Extemporaneous formulation (technology, analysis, application): method. rec. / T. G. Yarnykh, Fr. I. Tikhonov, I. S. Hryshchenko and others. - Kh., 2015. -379 p.
3. State Pharmacopoeia of Ukraine / State enterprise "Ukrainian Scientific Pharmacopoeia Center for the Quality of Medicinal Products" - 2nd edition. - Kharkiv: State Enterprise "Ukrainian Scientific Pharmacopoeia Center for the Quality of Medicinal Products", 2015. - Vol. 1. -1128 p.
4. Extraction of plant raw materials: training. Guide / Yu. I. Sidorov, I. I. Gubytska, R. T. Konechna, V. P. Novikov. – Lviv: View of the National Lviv Polytechnic University, 2018. - 336 p.
5. History of medicine and pharmacy: teaching. manual for pharmacy students. education closing and pharmacy Faculty of Higher Education of the Ministry of Health of Ukraine / A. A. Kotvitska, V. V. Gorbanev, O. O. Surikov and others. – Kharkiv: National Institute of Economics and Technology: Golden Pages, 2016. – 168 p.

## Slide 26
Thank you for attention!