## Slide 1: Practical lesson No. 8 Theme № 8. "Influence of HLB emulsifiers and production technology on quality parameters of emulsions. Types of emulsions. Types of instability of emulsions."

## Slide 2
Goal. The formation of students' theoretical knowledge about emulsifiers, the influence of the hydrophilic-lipophilic balance of emulsifiers on the technology of obtaining emulsions. Learn the physical and chemical properties of emulsifiers, types of emulsions and types of instability of emulsions.
Basic concepts. Hydrophilic-lipophilic balance (HLB) – is a number characterizing the effectiveness of the emulsifier. If the HLB number is within 3-6, a w/m emulsion is formed. Emulsifiers with a HLB number of 8-13 give an m/v emulsion. By changing the nature of the emulsifier and its concentration, it is possible to achieve phase reversal of the emulsion.

## Slide 3
Emulsions – are typically lyophobic dispersed systems. The loss of their aggregative stability can be due to the processes of isothermal distillation or coagulation (coalescence of drops) and is usually accompanied by a loss of sedimentation stability (layering of the system). The time of existence of a certain volume of the emulsion until its complete delamination can be taken as a measure of the stability of the emulsion.
Equipment: computer, multimedia equipment.

## Slide 4
Surface-active substances, due to their wide use, have considerable preventive and curative properties and are in great demand in the manufacture of creams for external use based on emulsions. The use of emulsion forms is due to their specific properties, such as the ability to combine oil and water phases, the possibility of introducing various active components, as well as good consumer properties.
Along with the classification of emulsifiers according to their chemical structure, there were attempts to make a classification according to their technological properties. In practice, we have to decide which emulsifier is most suitable for the emulsion we need. In the so-called system of hydrophilic-lipophilic balance (HLB) according to Griffin, all nonionic surfactants are assigned numerical values from 1 to 20. HLB gives information about the size and strength of hydrophilic and lipophilic groups in an amphiphilic substance. Low numerical values are assigned to lipophilic compounds, and higher numerical values to hydrophilic emulsifiers.

## Slide 5
For the HLB system, an equation was later developed, according to which the value of HLB can be approximately calculated based on the molecular weight of their hydrophobic part and the total weight of the emulsifier molecule.
HLB values are calculated based on the stoichiometric ratio of the lyophilic and hydrophilic parts of the molecule.
The relationship between the HLB value of some nonionic emulsifiers and their purpose is approximately as follows:
HLB 1–3 – as defoamers; HLB 3–8 – water-in-oil emulsifiers (cholesterol, cetearyl alcohol, lanolin alcohol, stearet-2, glyceryl stearate, sorbitan stearate);
HLB 7–9 – as winders; HLB 8–15 - as emulsifiers of the "oil in water" type (polysorbate-65, stearate-10, sucrose stearate, laureate-4, REG-8-stearate, sorbitan laurate);

## Slide 6
HLB 13–15 – as part of detergents;
HLB 15–20 – solubilizers (polysorbate-80, PEG-150 laurate, PEG-30 glyceryl laurate, PEG-40 – hydrogenated castor oil).
But nonionic surfactants do not obey the above laws, so it is better to determine their HLB values experimentally; they can significantly exceed the upper limit (20) of the HLB scale.
The advantage of the HLB system for the mixture of emulsifiers is that the value of the mixture of emulsifiers is additively composed of the fractions of the components:
HLBzag = HLB1x1 + HLB2x2 + HLB3x3 + ..., where x1, x2, x3 are mass fractions of individual components.

## Slide 7
This additivity also applies to the required HLB values, which are determined only experimentally. The required value of HLB is understood as the numerical value that an emulsifier or a mixture of emulsifiers should have, so that the dispersed oil phase has both optimal distribution and optimal stability. Thus, the value of HLB is attributed not only to emulsifiers, but also to substances that are emulsified.
In general, the value of HLB is only an aid for evaluating the possibilities of using emulsifiers. The use of only one HLB concept sometimes does not apply to cases of incompatibility of formulation components with the emulsifying base.

## Slide 8
The temperature of rotation is a feature of emulsions obtained with the help of nonionic emulsifiers. The conversion of a lipophilic emulsion (water-in-oil type) into a hydrophilic one (oil-in-water type) or vice versa is called phase rotation. Such a rotation is possible when the temperature changes. This is explained by the fact that ethoxylated nonionic emulsifiers change their hydrophilic-lipophilic properties, namely, the HLB value, depending on the temperature.

## Slide 9
It can be said that the ability of hydrophilic nonionic surfactants to stabilize direct emulsions (o/w) decreases with increasing temperature, and at the end, at a certain temperature, the emulsion turns into the opposite type (w/o). This temperature is called the phase rotation temperature. In ethoxylates, the TOF correlates with the cloud point. The latter refers to the temperature above which an aqueous solution of nonionic surfactants becomes cloudy, loses solubility and separates into two non-viscous isotropic phases.

## Slide 10
Phase inversion occurs when the water-soluble hydrate of the emulsifier splits off so much of its water of hydration that an oil-soluble emulsifier or oil-soluble hydrate is formed. Or vice versa, phase rotation occurs when an emulsifier dissolved in a non-aqueous medium forms a sufficiently water-soluble hydrate when water is added, and then the "water-in-oil" emulsion turns into an emulsion (o/w).
When the phases rotate, the interphase tension reaches a minimum, while the electrical conductivity also decreases sharply.

## Slide 11
Emulsions are typically lyophobic dispersion systems. The loss of their aggregative stability can be due to the processes of isothermal distillation or coagulation (coalescence of drops) and is usually accompanied by a loss of sedimentation stability (layering of the system). The time of existence of a certain volume of the emulsion until its complete delamination can be taken as a measure of the stability of the emulsion.
The stability of the emulsion is increased by introducing a stabilizer (emulsifier) into the system, as electrolytes, surfactants, and high-molecular compounds can be used. Aggregative stability of emulsions is determined by the same factors that cause resistance to coagulation of other lyophobic dispersed systems.

## Slide 12
Dilute emulsions can be quite stable in the presence of such weak emulsifiers as electrolytes. The stability of these emulsions is mainly due to the presence of a double electric layer on the particles of the dispersed phase. The stability of concentrated and highly concentrated emulsions in most cases is determined by the action of the structural-mechanical barrier during the formation of adsorption layers of the emulsifier. The formed interphase adsorption layers cause a smooth change in the properties of the transition zone at the boundary of the separation of two liquid phases, increasing the lyophilicity of the particles of the dispersed phase. The strongest stabilizing effect is created by high-molecular compounds and colloidal surfactants (soaps, nonionic surfactants), the adsorption layers of which have a gel structure and are highly hydrated.

## Slide 13
The type of emulsion formed during mechanical dispersion largely depends on the ratio of the volumes of the phases. A liquid contained in a larger volume usually becomes a dispersion medium. When dispersing equal volumes of two liquids, emulsions of both types appear, and the one with higher aggregative stability is preserved and is determined by the nature of the emulsifier. A special case is the stabilization of emulsions with highly dispersed powders. Such stabilization is possible with limited selective wetting of powders (at the edge angle θ is greater than 0°, but less than 180°). At the same time, the powders better stabilize the phase that is less wet. Thus, hydrophilic chalk "armors" the oil phase and prevents oil droplets from coalescing in an aqueous dispersion medium.

## Slide 14
Тests
1. Which of the emulsifiers is the most optimal for the production of a direct emulsion?
A potassium palmitate.
B In Kaolin.
C With Gelatin.
D Butanol.
E Plumbum oleate.
2. What is the name of the process of spontaneous clumping of droplets in emulsions?
A Coalescence.
B In Flocculation.
C Sedimentation.
D Flotation.
E Coagulation.

## Slide 15
3. All surface-active substances are concentrated on the surfaces of phase separation, forming adsorption layers. What is it connected with?
A due to amphiphilic properties,
B due to hydrophilic properties,
C due to hydrophobic properties,
D due to the absence of a lipophilic group,
E -.
4. For solubilization, mainly surfactants are used, indicators of the critical concentration of micelle formation, which have...
A low values,
B high values,
C presence of hygroscopicity and homogeneity of particles,
D presence of good solubility and wettability.

## Slide 16
5. Which emulsifiers in the process of their aggregation form multi-layered empty balls - vesicles?
A with two long hydrocarbon chains,
B with three short hydrocarbon chains,
C with one long hydrocarbon chain,
D with four short hydrocarbon chains.
E-.
6. Liposomes are spherical vesicles whose membranes consist of...
A of several double layers of amphiphilic lecithin molecules,
B of several double layers of hydrophobic structures,
C of one layer of lecithin,
D three layers of fat,
E fractional sklaud.

## Slide 17
7. What are the vesicles that form nonionic emulsifiers called?
A by niosomes;
B polysomes,
C trichosomes,
D sometimes
E -.
8. The most important representatives of ampholytic emulsifiers are...
A lecithins and phospholipids,
B fatty alcohols,
C stearins and unsaturated fatty acid esters,
D polyhydric alcohols,
E -.

## Slide 18
9. Choose a substance that will optimally stabilize the type emulsion
"oil-water":
A Casein,
B Ethanol,
C Benzene,
D Potassium chloride.
E -
10. What amount (cm3) of toluene must be mixed with water containing sodium oleate to obtain 100 cm3 of a concentrated emulsion?
A from 0.1 to 74.0 cm3
B from 10.0 to 75.0 cm3
C is more than 75.0 cm3
D from 74.0 to 90.0 cm3
E to 0.1 cm3

## Slide 19
3.1. Tasks for fixing the material
№№ c.e. | Mein Tasks | Instructions | Answers
1 | 2 | 3 | 4
1. | Classification of emulsions. | your answer | 
2. | Basic criteria of emulsifiers. | your answer | 
3. | Physico-chemical properties of emulsifiers. | your answer | 
4. | Application of emulsions. | your answer | 
5. | Methods of obtaining emulsions. | your answer | 
6. | Surfactants | your answer | 
7. | Emulsions as liquid systems | your answer | 
8. | Temperature of rotation in emulsions. | your answer | 
9. | Types of emulsions. | your answer | 
10. | Types of instability of emulsions. | your answer | 

## Slide 20
3.2. Questions for self-control:
1. What dispersed systems are called emulsions?
2. Can any liquids form an emulsion?
3. 3. How are emulsions classified? Their practical application.
4. What substances are called emulsifiers?
5. How do emulsifiers stabilize emulsions?
6. Methods of obtaining emulsions.
7. What is the circulation of phases of emulsions? Under what conditions does it occur?
8. What are the methods of breaking emulsions? What are they based on?
9. Why does water poured into it not flow out of a sieve (diameter of holes 1 mm), covered with a thin layer of paraffin?
10. Nonionic surfactants, amphoteric and cationic surfactants. The principle of their action and use.

## Slide 21
Basic literature:
1. Gladukh E.V. Theoretical foundations of pharmaceutical technology. Study guide for extracurricular independent work / E.V. Gladukh, I.V. Saiko, A.A. Sichkar, D.P. Soldatov. Kh.: NFaU, 2016. - 202 p.
2. Technology of drugs of industrial production (vol. 2 of 2). Chuyeshov V. I., Gladukh E. V., Saiko I. V., Lyapunova O. O., Sichkar A. A., Krutskikh T. V., Ruban O. A. Kh.: National University of Applied Sciences; Golden Pages, 2013. - 638 p.
3. Technology of drugs of industrial production (vol. 1 of 2). Chuyeshov V. I., Gladukh E. V., Saiko I. V., Lyapunova O. O., Sichkar A. A., Krutskikh T. V., Ruban O. A. Kh.: National University of Applied Sciences; Golden Pages, 2012. - 694 p.
List of recommended literature (main, additional, electronic information resources):

## Slide 22
Additional literature:
1. Technological equipment of the pharmaceutical and biotechnological industry: tutorial. for university students education closing III-IV accreditation level / M.V. Stasevych and others; 2nd ed., revision. and added – Lviv: Novy svit-2000, 2018. – 410 p.
2. Yarnykh, T. G. Extemporaneous formulation (technology, analysis, application): method. rec. / T. G. Yarnykh, Fr. I. Tikhonov, I. S. Hryshchenko and others. - Kh., 2015. -379 p.
3. State Pharmacopoeia of Ukraine / State enterprise "Ukrainian Scientific Pharmacopoeia Center for the Quality of Medicinal Products" - 2nd edition. - Kharkiv: State Enterprise "Ukrainian Scientific Pharmacopoeia Center for the Quality of Medicinal Products", 2015. - Vol. 1. -1128 p.
4. Extraction of plant raw materials: training. Guide / Yu. I. Sidorov, I. I. Gubytska, R. T. Konechna, V. P. Novikov. – Lviv: View of the National Lviv Polytechnic University, 2018. - 336 p.
5. History of medicine and pharmacy: teaching. manual for pharmacy students. education closing and pharmacy Faculty of Higher Education of the Ministry of Health of Ukraine / A. A. Kotvitska, V. V. Gorbanev, O. O. Surikov and others. – Kharkiv: National Institute of Economics and Technology: Golden Pages, 2016. – 168 p.

## Slide 23
Thank you for attention!