## Slide 1: Topic 7. Organization of activities for validating production processes and qualifying equipment and auxiliary systems in organizations that are pharmaceutical market entities.
Odessa National Medical University
Department of General and Clinical Pharmacology and Pharmacognosy
Discipline «Qualiti systems in pharmacy»
Lecturer: Eberle L.V.
Candidate of Biological Sciences, Associate Professor of the Department of General and Clinical Pharmacology and Pharmacognosy

## Slide 2
The relevance of the topic. According to the requirements of good manufacturing practice, there must be a documented general policy of the manufacturer regarding intentions and approach to validation, as well as persons responsible for the development, verification, approval, and documentation of each stage of validation.
Objective: to provide higher education students with theoretical knowledge regarding the organization of activities related to the validation of manufacturing processes and the qualification of equipment and auxiliary systems in organizations within the pharmaceutical market.
Lecture plan and organizational structure:
Validation: definition of concepts, objects, types.
Validation staffing.
Validation documents.
Validation of analytical methods.
Cleaning validation.
Qualification: definition of concepts, objects.
Qualification stages.

## Slide 3
Validation: definition of concepts, objects, types
Validation is the actions that, according to the principles of good manufacturing practice, demonstrate that a certain methodology, process, equipment, raw material, activity, or system actually yield the expected results.
Objects:
  technological process (for each name of medicinal product);
  methods of quality control (analytical methods);
  cleaning procedures;
  methods of in-process control testing;
  computerized systems.

## Slide 4
Process validation can be defined as documented evidence that the process, operated within established parameters, can perform effectively and reproducibly to produce a medicinal product meeting its predetermined specifications and quality attributes.
Prospective validation is validation carried out before routine production of products intended for sale.
Concurrent validation is validation carried out in exceptional circumstances, justified on the basis of significant patient benefit, where the validation protocol is executed concurrently with commercialisation of the validation batches.
Re-validation is the repetition of process validation to ensure that changes to the process/equipment made in accordance with change control procedures have not adversely affected process characteristics and product quality.
Qualification is actions that confirm that specific equipment is operating correctly and indeed producing the expected results. The concept of "validation" is broader and sometimes includes the concept of "qualification".

## Slide 5
Validation staffing
At the enterprise, there should be a formed validation committee whose main task is to manage validation activities.
For each object, a validation group should be formed.
The main tasks of the validation groups are:
Preparation for testing (compilation of test protocols, etc.).
Conducting tests, documenting, recording deviations, changes, non-compliances.
Interpreting results, their formalization and analysis, preparation of conclusions and recommendations, preparation of a report.

## Slide 6
Validation documents
1. Validation Master Plan
The Validation Master Plan establishes a list of objects subject to validation, defines personnel responsibilities, specifies the frequency of validation activities, and outlines documentation requirements.
The Validation Master Plan should include:
  the purpose of validation;
  an organizational scheme for validation activities;
  a list of all facilities, systems, equipment, and processes that require qualification/validation;
  the form of documentation to be used for protocols and reports;
  planning and execution schedule;
  changes control;
  references to existing documents.

## Slide 7
2. Validation measurement protocol
This document describes the subject of qualification/validation, the type of validation being conducted (e.g., retrospective, prospective, concurrent), lists the measuring instruments to be used, the number of production cycles required for validation, critical process parameters, critical quality attributes, and associated acceptance criteria.
Critical quality attribute (CQA) is a physical, chemical, biological or microbiological property or characteristic that should be within an approved limit, range or distribution to ensure the desired product quality.
Critical process parameter (CPP) is a process parameter whose variability has an impact on a critical quality attribute and therefore should be monitored or controlled to ensure the process produces the desired quality.
Acceptance criteria are numerical limits, intervals, or other relevant criteria for accepting the results of tests.

## Slide 8
3. Validation Report
A document containing cross-references to the validation protocol and summarizing the obtained results, explaining any deviations identified with corresponding conclusions, including recommended changes to correct deficiencies. Any deviations from the validation protocol must be documented with appropriate justification.
Validation of Analytical Methods
If the analytical methods used are not included in the European Pharmacopoeia, or any other relevant pharmacopoeia, they must undergo validation.
The methodology for validation of analytical methods involves the determination of the following typical validation characteristics.
Specificity is the ability to assess unequivocally the analyte in the presence of components which may be expected to be present. Typically these might include impurities, degradants, matrix, etc.
The accuracy of an analytical procedure expresses the closeness of agreement between the value which is accepted either as a conventional true value or an accepted reference value and the value found.

## Slide 9
The precision of an analytical procedure expresses the closeness of agreement between a series of measurements obtained from multiple sampling of the same homogeneous sample under the prescribed conditions. The precision of an analytical method is usually characterized by the standard deviation or relative standard deviation for a series of measurements.
The detection limit of an individual analytical procedure is the lowest amount of analyte in a sample which can be detected but not necessarily quantitated as an exact value.
The quantitation limit of an individual analytical procedure is the lowest amount of analyte in a sample which can be quantitatively determined with suitable precision and accuracy. The quantitation limit is a parameter of quantitative assays for low levels of compounds in sample matrices, and is used particularly for the determination of impurities and/or degradation products.
The linearity of an analytical procedure is its ability to obtain test results which are directly proportional to the concentration of analyte in the sample.
The range of an analytical procedure is the interval between the upper and lower concentration of analyte in the sample for which it has been demonstrated that the analytical procedure has a suitable level of precision, accuracy and linearity.
The robustness of an analytical procedure is a measure of its capacity to remain unaffected by small, but deliberate variations in method parameters and provides an indication of its reliability during normal usage.

## Slide 10
Сleaning validation
Cleaning validation is documented evidence that an approved cleaning procedure will reproducibly remove the previous product or cleaning agents used in the equipment below the scientifically set maximum allowable carryover level.
Typically, cleaning validation should target stages of the process where contamination or carryover of materials pose the greatest risk to API quality. For example, validation of equipment cleaning procedures may not be necessary at the initial stages of the process if residues are removed in subsequent cleaning stages.
If different APIs or intermediate products are manufactured on the same equipment, cleaning validation takes into account the solubility data of residues and the complexity of equipment cleaning, as well as the maximum residue limits, considering their activity, toxicity, and stability.
Cleaning procedures should be monitored at appropriate intervals after validation to ensure that these procedures are effective when used in a routine manufacturing process.

## Slide 11
Qualification: definition of concepts, objects
Qualification is actions that confirm that specific equipment is operating correctly and indeed producing the expected results.
Objects:
technical systems, including: premises, classified and non-classified according to cleanliness classes;
main technological equipment;
quality control equipment;
engineering systems ensuring production operation (water for pharmaceutical purposes, clean steam, process gases).
Before commencing the process validation activities, it is necessary to complete the proper qualification of equipment and auxiliary systems.

## Slide 12
Qualification stages
User requirements specification (URS)
The specification for equipment, facilities, utilities or systems should be defined in a URS. The essential elements of quality need to be built in at this stage and any GMP risks mitigated to an acceptable level.
The URS should be a point of reference throughout the validation life cycle.
Design qualification (DQ)
It is the documented verification that the proposed design of the facilities, systems and equipment is suitable for the intended purpose. The requirements of the user requirements specification should be verified during the design qualification.
Compliance of the design with GMP should be demonstrated and documented at this stage.
Factory acceptance testing (FAT) / Site acceptance testing (SAT)
Equipment, especially if incorporating novel or complex technology, may be evaluated, if applicable, at the vendor prior to delivery.

## Slide 13
Where appropriate and justified, documentation review and some tests could be performed at the FAT or other stages without the need to repeat on site if it can be shown that the functionality is not affected by the transport and installation.
FAT may be supplemented by the execution of a SAT following the receipt of equipment at the manufacturing site.
Prior to installation, equipment should be confirmed to comply with the URS at the vendor site.
Installation qualification (IQ)
It is the documented verification that the facilities, systems and equipment, as installed or modified, comply with the approved design and the manufacturer’s recommendations.
Operational qualification (OQ)
It is the documented verification that the facilities, systems and equipment, as installed or modified, perform as intended throughout the anticipated operating ranges.
OQ should include tests to confirm upper and lower operating limits, and/or "worst-case" conditions.

## Slide 14
Performance qualification (PQ)
It is the documented verification that systems and equipment can perform effectively and reproducibly based on the approved process method and product specification.
PQ should include:
Tests, using production materials, qualified substitutes or simulated product proven to have equivalent behaviour under normal operating conditions with worst case batch sizes.
Tests should cover the operating range of the intended process.
Re-qualification
Equipment, facilities, utilities and systems should be evaluated at an appropriate frequency to confirm that they remain in a state of control.

## Slide 15
Topic 8. Audits of pharmaceutical quality systems.

## Slide 16
Concept of audit, classification of audits, audit criteria and evidence
The procedure for conducting audits of the functioning of a pharmaceutical enterprise (systematic analysis of the system) is defined by GMP rules and the requirements of ISO 9001:2015 Quality management systems. Requirements. Guidelines for conducting management system audits and evaluating the competence of persons involved in the audit process are presented in the standard ISO 19011:2018 Guidelines for auditing management systems.
Audit is systematic, independent and documented process for obtaining audit evidence and evaluating it objectively to determine the extent to which the audit criteria are fulfilled.
Classification of audits
Internal audits (first party audits) are conducted by the organization itself, or on its behalf, for management review and other internal purposes.
External audits include second and third party audits.
Second party audits are conducted by parties having an interest in the organization, such as customers, or by other persons on their behalf.
Third party audits are conducted by independent auditing organizations, such as regulators or those providing certification.
Combined audit is carried out together at a single auditee (organization as a whole or parts there of being audited) on two or more management systems.
Joint audit is conducted at a single auditee by two or more auditing organizations.

## Slide 17
Audit criteria and evidence
Audit criteria are set of requirements used as a reference against which objective evidence is compared.
Audit evidence records, statements of fact or other information, which are relevant to the audit criteria and verifiable.
Audits are conducted to determine compliance with a range of audit criteria, either separately or in combination:
requirements defined in one or more management system standards;
policies and requirements defined by relevant interested parties;
legal and regulatory requirements.

## Slide 18
Principles of auditing
Conducting an audit is based on 7 principles:
1. Adherence to ethical norms — the foundation of professionalism. Auditors and the person managing an audit programme should:
  perform their work with honesty, diligence, and responsibility;
  demonstrate their competence while performing their work;
  perform their work in an impartial manner, i.e. remain fair and unbiased in all their dealings;
  be able to withstand any pressure that could influence their judgments during the audit.
  2. Honesty in reporting results — the obligation to report truthfully and accurately.
Audit findings, audit conclusions and audit reports should reflect truthfully and accurately the audit activities. Significant obstacles encountered during the audit and unresolved diverging opinions between the audit team and the auditee should be reported.
3. Due professional care — the demonstration of diligence and prudence during the audit. Auditors should exercise due care in accordance with the importance of the task they perform and the confidence placed in them by the audit client and other interested parties.
An important factor in carrying out their work with due professional care is having the ability to make reasoned judgements in all audit situations.

## Slide 19
4. Confidentiality — protection of information.
Auditors should exercise discretion in the use and protection of information acquired in the course of their duties.
5. Independence — the principle of impartiality in auditing and objectivity of audit conclusions.
Auditors should be independent of the activity being audited wherever practicable, and should in all cases act in a manner that is free from bias and conflict of interest.
6. Evidence-based approach — a rational method for forming reliable and reproducible audit conclusions in a systematic audit process.
Records, factsheets, or other information related to audit criteria (audit evidence) should be verifiable.
7. Risk-based approach — an approach to auditing that considers risks and opportunities.
The risk-based approach significantly influences the planning, conduct of audits, and preparation of audit reports to ensure that audits focus on issues important to the audit client.

## Slide 20
The diagram illustrates the process flow for the management of an audit programme, including performing an audit

## Slide 21
Audit programme – the arrangements for a set of one or more audits planned for a specific time frame and directed towards a specific purpose.
1. Process flow for the management of an audit programme
1.1. Establishing the audit programme objectives
The audit client (organization or person requesting an audit) should ensure the establishment of the audit programme objectives.
These objectives can be based on consideration of the following:
needs and expectations of interested parties, including customers;
management system requirements;
need for supplier evaluation;
risks to the auditee and auditee’s level of performance;
results of previous audits.
1.2. Determining and evaluating audit programme risks and opportunities
The person managing the audit programme should identify and describe to the audit client the risks, as well as the requirements for resources, so that they can be properly taken into account.
1.3. Establishing audit programme
The person managing the audit programme should determine the scope of the audit programme and the resources of the audit programme (financial and time resources, availability of auditors and technical experts whose competence corresponds to the specific objectives of the audit programme, etc.).

## Slide 22
  1.4. Implementing audit programme
The person managing the audit programme should implement the audit programme by means of the following:
communicating the pertinent parts of the audit programme to relevant parties and informing them periodically of its progress;
coordinating and scheduling audits and other activities relevant to the audit programme;
ensuring the selection of audit teams with the necessary competence;
providing necessary resources to the audit teams;
ensuring that audit activities are recorded and records are properly managed and maintained.

## Slide 23
Audit methods
Based on location of the auditor:
On-site audit activities are performed at the location of the auditee, involving:
  Conducting interviews.
  Completing checklists and questionnaires with auditee participation.
  Conducting document review with auditee participation.
  Sampling.
Remote audit activities are performed at any place other than the location of the auditee, regardless of the distance via interactive communication means.
Based on the level of involvement of the auditor and the auditee:
Interactive audit activities involve interaction between the auditee’s personnel and the audit team.
Non-interactive audit activities involve no human interaction with persons representing the auditee but do involve interaction with documentation.

## Slide 24
  1.6. Monitoring audit programme
The person managing the audit programme should monitor its implementation considering the need to:
evaluate conformity with audit schedules;
evaluate the ability of the audit teams to implement the audit plan;
evaluate feedback from auditees and auditors.
  2. Reviewing and improving audit programme
The person managing the audit programme should review the audit programme to assess whether its objectives have been achieved.
2.1. Process flow for the performing an audit
  Initiating audit
When an audit is initiated, the responsibility for conducting the audit remains with the assigned audit team leader until the audit is completed.
The initial contact with the auditee for the performance of the audit should be made by the audit team leader. The purposes of the initial contact are the following:
establish communications with the auditee’s representatives;
confirm the authority to conduct the audit;
provide information on the audit objectives, scope, methods and audit team composition, including technical experts;
confirm the agreement with the auditee regarding the extent of the disclosure and the treatment of confidential information;
make arrangements for the audit including scheduling the dates.

## Slide 25
  2.2. Preparing audit activities
  2.2.1. Performing document review in preparation for the audit
The relevant management system documentation of the auditee should be reviewed in order to gather information to prepare audit activities.
2.2.2 Preparing the audit plan
The audit team leader should prepare an audit plan based on the information contained in the audit programme and in the documentation provided by the auditee.
The audit plan should cover or reference the following:
      the audit objectives;
      the audit scope, including identification of the organizational and functional units, as well as processes to be audited;
      the audit criteria and any reference documents;
      the locations, dates, expected time and duration of audit activities to be conducted, including meetings with the auditee’s management;
      the audit methods to be used;
      the roles and responsibilities of the audit team members, as well as guides and observers.

## Slide 26
    2.2.3 Assigning work to audit team
The audit team leader, in consultation with the audit team, should assign to each team member responsibility for auditing specific processes, activities, functions or locations.
    2.2.4. Preparing work documents
The audit team members should collect and review the information relevant to their audit assignments and prepare work documents.
  2.3. Conducting the audit activities
  2.3.1. Assigning roles and responsibilities of guides and observers
Guides and observers may accompany the audit team with approvals from the audit team leader, audit client and/or auditee. Their responsibilities should include the following:
assisting the auditors in identifying individuals to participate in interviews and confirming timings and locations;
arranging access to specific locations of the auditee.
2.3.2. Conducting the opening meeting
The purpose of the opening meeting is to:
      confirm the agreement of all parties to the audit plan;
      introduce the audit team;
      ensure that all planned audit activities can be performed.

## Slide 27
    2.3.3. Communicating during audit
During the audit, the audit team leader should periodically communicate the progress of the audit and any concerns to the auditee. Evidence collected during the audit that suggests an immediate and significant risk to the auditee should be reported without delay to the auditee.
    2.3.4. Audit information availability and access
Where, when and how to access audit information is crucial to the audit. The location is where the information needed for the specific audit activity is available to the audit team. This may include physical and virtual locations.
    2.3.5. Reviewing documented information while conducting audit
The auditee’s relevant documented information should be reviewed to determine the conformity of the system, as far as documented, with audit criteria.
    2.3.6. Collecting and verifying information
During the audit, information relevant to the audit objectives, scope and criteria should be collected by means of appropriate sampling and should be verified, as far as practicable.
    2.3.7. Generating audit findings
Audit evidence should be evaluated against the audit criteria in order to determine audit findings. Audit findings can indicate conformity or nonconformity with audit criteria. Nonconformities and their supporting audit evidence should be recorded.

## Slide 28
    2.3.8. Determining audit conclusions
Audit conclusions should address issues such as the extent of conformity with the audit criteria and robustness of the management system.
Any diverging opinions regarding the audit findings or conclusions between the audit team and the auditee should be discussed and, if possible, resolved. If not resolved, this should be recorded.
  2.4. Preparing and distributing audit report
The audit team leader should report the audit conclusions in accordance with the audit programme. The audit report should then be distributed to the recipients as defined in the audit programme.
  2.5. Completing audit
The audit is completed when all planned audit activities have been carried out.
3. Conducting audit follow-up
The outcome of the audit can, depending on the audit objectives, indicate the need for corrections, or for corrective actions, or opportunities for improvement. Such actions are usually decided and undertaken by the auditee within an agreed timeframe. The completion and effectiveness of these actions should be verified. This verification may be part of a subsequent audit.

## Slide 29
Thank you for your attention!